## Slide 1: SIMULATION OF WORD MULTIPLIER
2K19/CO/319
RITIK SINGH
INNOVATIVE PROJECT REPORT
USING BOOTH ALGORTIHM

## Slide 2: About the Project
The project is about simulating a word multipler to provide a physically compact high speed and low power consumption unit. 
Being a core part of ALU, multipliers are in extremely high demand on its speed and low power consumption.
Multipliers play an important role in today’s digital signal processing and various other applications.

## Slide 3: Objective:
The purpose of this project is to model and simulate hardware multiplication using Booth algorithm for multiplication.

## Slide 4: Introduction
A binary multiplier is an electronic circuit used in digital electronics, such as a computer, to multiply two binary numbers.
The two numbers are more specifically known as multiplicand and multiplier and the result is known as product.
The multiplicand & multiplier can be of various bit size. The product’s bit size depends on the bit size of the multiplicand & multiplier. The bit size of the product is equal to the sum of the bit size of multiplier & multiplicand.
It is built using binary adders.
A variety of computer arithmetic techniques can be used to implement a digital multiplier.
Most techniques involve computing a set of partial products, and then summing the partial products together.

## Slide 5: ADDERS
In electronics, an adder is a digital circuit that performs addition of two or more numbers.
Adders can be constructed for many numerical representations, such as Binary-coded decimal or excess-3 
Adders are different types in generally

## Slide 6: HALF ADDER
The half adder adds two single binary digits A and B. 
It has two outputs, sum (S) and carry (C).

## Slide 7: FULL ADDER 
Adding two single-bit binary values, X, Y along with a carry input bit C-in and
produces a sum bit S and a carry out C-out bit.

## Slide 8: Adder Example
Example: Consider an example of multiplication of two numbers, say A and B (2 bits each), C
= A x B. 
The first partial product is formed by multiplying the B1B0 by A0. The multiplication of two
bits such as A0 and B0 produces a 1 if both bits are 1; otherwise it produces a 0 like an
AND operation. So the partial products can be implemented with AND gates.
The second partial product is formed by multiplying the B1B0 by A1 and is shifted one
position to the left.

## Slide 9: Adder Example

## Slide 10: MULTIPLICATION ALGORITHM
Multiplication process has three main steps:
Partial product generation
Partial product reduction
Final addition.
The common multiplication method is the “add and shift “algorithm.

## Slide 11
Booths Algorithm for Multiplication
A : It represents the Accumulator which stores the partial
product, It is initialized with Zero (0)
M: It represents the multiplicand
Q: It represents the multiplier,
Q0: it represents the LSB of Q
Q−1 : It represents a Flip Flop which is initialized with Zero(0)
Count: It represents the counter(number of bits in M or Q)
Note: In Arithmetic Shift Right, We copy the sign bit of the
number in MSB

## Slide 12: Working on the Booth Algorithm
Set the Multiplicand and Multiplier binary bits as M and Q, respectively.
Initially, we set the AC and Qn + 1 registers value to 0.
SC represents the number of Multiplier bits (Q), and it is a sequence counter that is continuously decremented till equal to the number of bits (n) or reached to 0.
A Qn represents the last bit of the Q, and the Qn+1 shows the incremented bit of Qn by 1.
On each cycle of the booth algorithm, Qn and Qn + 1 bits will be checked on the following parameters as follows:
i. When two bits Qn and Qn + 1 are 00 or 11, we simply perform the arithmetic shift right operation (ashr) to the partial product AC. And the bits of Qn and Qn + 1 is incremented by 1 bit.
ii. If the bits of Qn and Qn + 1 is shows to 01, the multiplicand bits (M) will be added to the AC (Accumulator register). After that, we perform the right shift operation to the AC and QR bits by 1.
iii. If the bits of Qn and Qn + 1 is shows to 10, the multiplicand bits (M) will be subtracted from the AC (Accumulator register). After that, we perform the right shift operation to the AC and QR bits by 1.
The operation continuously works till we reached n - 1 bit in the booth algorithm.
Results of the Multiplication binary bits will be stored in the AC and QR registers.

## Slide 13: Example:
Let us take an example of multiplying two binary numbers as follows. The process is similar to multiplying two decimal numbers, with a difference that the resulting numbers are all binary.
110 = 6
X 011 = 3
-------------------------
1 1 0 ; 110 X 1 (Shifted one position left)
1 1 0 x ; 110 X 1 (Shifted one position left)
0 0 0 x x ; 110 X 0 (Shifted one position left)
-------------------------
1 0 0 1 0 = 18

## Slide 14: OUTPUT:
CODE IN THE WORD FILE.

## Slide 15: APPLICATIONS OF MULTIPLIERS
These are most commonly used in various applications especially in the field of digital signal processing to perform the various algorithms.
Array multiplier is used to perform the arithmetic operation, like filtering, Fourier transform, image coding.
Commercial applications like computers, mobiles, high speed calculators and some general purpose processors require binary multipliers.
High-speed operation.

## Slide 16: Bibliography:
https://en.wikipedia.org/wiki/Binary_multiplier#:~:text=A%20binary%20multiplier%20is%20an,to%20implement%20a%20digital%20multiplier.
https://en.wikipedia.org/wiki/Multiplication_algorithm
https://vlsiuniverse.blogspot.com/2013/05/binary-multiplier.html#:~:text=Binary%20multiplication%20process%3A%20A%20Binary,provide%20the%20result%20as%20output.&text=The%20two%20numbers%20A1A0%20and,a%204%2Dbit%20output%20P3P2P1P0.
https://www.cs.columbia.edu/~martha/courses/3827/sp11/slides/2bit_multiplier_soln.pdf
https://www.electricaltechnology.org/2018/05/binary-multiplier-types-binary-multiplication-calculator.html
https://technobyte.org/multiplier-2-bit-3-bit-digital/
https://electronics.stackexchange.com/questions/99813/3-bit-multipliers-how-do-they-work/99837
https://inst.eecs.berkeley.edu/~eecs151/sp18/files/Lecture21.pdf
https://www.electronicshub.org/binary-multiplication/
https://www.sciencedirect.com/topics/engineering/binary-multiplication
https://en.wikipedia.org/wiki/Binary_multiplier

## Slide 17: THANK YOU